## Slide 1: Cash Flow Estimation Models
Estimating Relationships and Problems

## Slide 2: Engineering Economic Analysis - Seven Steps
1. Recognition and formulation of the problem.
2. Development of the feasible alternatives.
3. Development of the net cash flows (and other prospective outcomes) for each alternative.
4. Selection of a criterion (or criteria) for determining the preferred alternative.
5. Analysis and comparison of the alternatives.
6. Selection of the preferred alternative.
7. Performance monitoring and post-evaluation.
Notes: Steps 1 and 2 are done in any design project
Steps 4-6 were discussed during the first half of the semester
Steps 3 is the focus of this lecture

## Slide 3: Developing Net Cash Flows for Each Alternative
Because engineering economy studies deal with outcomes that extend into the future, estimating the future cash flows for feasible alternatives is a critical step in the analysis procedure.

## Slide 4: Estimating Techniques
Indexes
Unit Technique
Factor Technique
Estimating Relationships
  Power-Sizing Technique
  Learning Curve
Analysis of product price and cost
  Establishing product price as a markup to cost
  Establishing price in relation to competition

## Slide 5: Indexes
An index is a dimensionless number that indicates how a cost or a price has changed with time (typically escalated) with respect to the base year.
Cn = cost or selling price of an item in year n
Ck = cost or price of the item at an earlier point in time (say year k)
In = index value in year n
Ik = index value in year k
Cn = Ck (In /Ik )
Do Problem 1

## Slide 6: Example 1
A certain index for the cost of purchasing and installing utility boilers is keyed to 1974, where its baseline value was set at 100. Company XYZ installed a 50,000 lb/hr in 1989 for $350,000 when the index had value of 312. This same company must install another boiler of the same size in 1996. The index in 1996 is 468.
Approximate cost of new boiler =
C1996 = $350,000 (468/312) = $525,000

## Slide 7: Unit Technique
Involves a “per unit factor” that can be estimated effectively.
Examples:
  Capital cost of a plant per kilowatt of capacity
  Revenue per customer served
  Operating cost per mile
  Construction cost per square foot
  Maintenance cost per hour
Do problem 2

## Slide 8: Example 2
We need a preliminary estimate of the cost of a particular house. Use the factor of, say, $55 per square foot and assume that the house is approximately 2,000 square feet.
Estimated cost of the house =
  $55 x 2,000 = $110,000

## Slide 9: Factor Technique
The factor technique is an extension of the unit technique
C = cost being estimated
Cd = cost of the selected component d that is estimated directly
fm = cost per unit of component m
Um = number of units of component m
C =  Cd +  fm Um
d m

## Slide 10: Example 3
We need a refined estimate of the cost of the house. Assume that the house is approximately 2,000 square feet of living space, has one porch and two garages Use the factor of, say, $50 per square foot of living space, $5,000 per porch and $8,000 per garage.
Estimated cost of the house =
  $50 x 2,000 + $5,000 + ($8,000 x 2)= $121,000

## Slide 11: Power-Sizing Technique
Also sometimes referred to as the exponential model
Often used to cost industrial plants and equipment
CA = cost for plant A
CB = cost for plant B
SA = size of plant A
SB = size of plant B
X = cost-capacity factor to reflect economies of scale CA /CB = (SA /SB )X
or CA = CB (SA /SB )X

## Slide 12: Example 4
Make a preliminary estimate of the cost of building a 600-MW fossil fuel power plant. It is known that a 200-MW plant cost $100 million 20 years ago when the appropriate cost index was 400. That cost index is now 1,200. The power-sizing factor is 0.79.
Today’s estimated cost of a 200-MW plant =
  $100 million x (1,200/400) = $300 million
Today’s estimated cost of a 600-MW plant =
  $300 million x (600/200)0.79 = $714 million

## Slide 13: Learning Curves
Mathematical model that explains the phenomenon of increased worker efficiency and improved performance through repetitive production
Also called experience curves or manufacturing progress functions
Was first reported in 1936 by T.P. Wright, an aerospace engineer
He observed that, with each doubling of cumulative production, the total man-hours needed per plane were reduced to 80% of the former level.

## Slide 14: Learning Curve Example

## Slide 15: Mathematics of the Learning Curve
u = the output unit number
Zu = the number of input resources needed to produce output unit number u
K = the number of input resources needed to produce the first output unit
s = the learning curve slope parameter
Zu = Ksa where a = 0,1,2,3,....
and u = 2a
or,
Zu = Kun where n = log s / log 2

## Slide 16: Example 5
A student team is designing a formula car for national competition. The time required for the team to assemble the first car is 100 hours. Their learning rate is 0.8.
The time it will take to assemble the 10th car =
Z10 = 100 (10) log 0.8/log2
= 100 (10) -0.322 = 100 / 2.099
= 47.6 hours

## Slide 17: Example 6
A rare product is made in batches of 50 units. Within a batch, each unit take less and less time to be produced because of a learning process of 75%.
The time needed to assemble the first unit = 2.3123 hrs
The time needed to assemble additional units is
Zu = 2.3123 (u) log 0.75/log2
= 2.3123 (u) -0.415
The total time taken for all 50 units =
Z1 + Z2 + Z3 +...+ Z50 = 36.48 hours

## Slide 18: Determining the per unit product cost estimate using a bottom-up approach
Construct a table containing per unit estimates, factor estimates, and direct estimates
Start with labor costs
Compute indirect costs to get the total manufacturing cost
Divide by the number of units for the per unit cost
Account for margin of profit
This is referred to as the design to price approach

## Slide 19: Example 7
Direct labor costs are estimated via the unit technique. 36.48 direct labor hours are required to produce 50 units and the composite labor rate is $10.54 per hour.
Indirect costs are often allocated using factor estimates. Planning labor and quality control are estimated at 12% and 11% of direct labor cost

## Slide 20
Factory overhead and general and administrative expenses are estimated as 105% and 15% of total labor costs
Total production materials cost for the 50 unit is $167.17. A direct estimate of $28.00 applied to outside manufacturing

## Slide 21
Packing costs are estimated as 5% of all previous costs
Costs of other miscellaneous charges are figured in as 1% of the current subtotal
Facility rental is estimated at $0.

## Slide 22
The price of a product is based on the overall cost of making the item plus a built-in profit (profit margin)
Here we use a profit margin of 10%

## Slide 23: Target Costing
used by Japanese firms
top-down approach
focuses on “what should the product cost” rather than “what does the product cost”
begins with market surveys to determine competitor’s price
target cost(1 + Profit Margin) = competitor’s price
target cost = competitor’s price/(1 + Profit Margin)
Target cost is used as a goal for engineering design, procurement, and production

## Slide 24: Example 6 (cont’d)
Competitor’s price is $27.50. ROS = 10%. Thus
target cost = $27.50 (1-0.1) = $24.75
Since Unit Selling Price > Target Cost, we must work backwards from the Total Mnfg Cost to reduce it

## Slide 25: Summary
Developing cash flows for each alternative in a study is a pivotal step in the engineering economic analysis procedure.
An integrated approach for developing cash flows includes
  determining the length of the analysis period
  fixing a perspective and determining a baseline
  a WBS definition of the project
  a cost and revenue structure
  estimating techniques (models)

## Slide 26: Workbook Problem 1
Manufacturing equipment was purchased in 1991 for $200,000. What was the estimated cost in 1996?
C1996 = C1991 (I1996/ I1996 )
= $200,000 (293/223) = $262,780.27

## Slide 27: Workbook Problem 2
10 miles of poles and lines are needed.
Each mile of line costs $14,000
Each pole (placed every 40 yards) costs $210.
Number of poles needed =
10 miles/ 40 yards per pole =
(10 miles)(5280 ft/miles)(1 yd/3 ft)/(40 yd/pole)
= 440 poles
Cost = (10 mi)($14,000/mi) + (440 poles) ($210/pole)
= $232,400

## Slide 28: Workbook Problem 3
Initial work K = 126 hours
Assume learning curve s = 95%
n = log 0.95/log 2 = -0.074
Z8 = 126 (8)–0.074 =108 hours
Z50 = 126 (50)–0.074 =94.3 hours
Average for first five = (Z1+Z2+Z3+Z4+Z5)/5 =
126 (1–0.074 +2–0.074 +3–0.074 +4–0.074 +5–0.074 ) /5 = 117.5

## Slide 29: Workbook Problem 4
Initial cost K = $1.15X
Assume learning curve s = 85%
n = log 0.85/log 2 = -0.152
Z30 = 1.15X (30) –0.152 =0.686X
After 30 months, a 31.4% (100%-68.6%) reduction in overhead costs is expected (with respect to the current cost X)

## Slide 30: Workbook Problem 5
Let’s build a spreadsheet