## Slide 1: Replacement Analysis
Impact of Taxes on Replacement Decisions

## Slide 2: Replacement Analysis Questions
Do we replace now or later?
How do taxes impact the decisions?
Examples
  Example 3: When the useful lives of the defender and the challenger are known and the same
  Example 4: When the useful lives of the defender and the challenger are not known or are not the same

## Slide 3: Example 3: Known and Equal Lives
Existing Pump A (defender) | 
Capital investment when purchased 5 years ago: | $17,000
Useful life: | Another 9 years
Depreciation: | SL with half-year convention over 9 yrs
Annual Expenses | 
Replacement of impeller and bearings | $1,750
Operating and maintenance | $3,250
Taxes and insurance ($17,000 x 2%) | $340
 | $5,340
Present Market Value | $750
Estimated Market Value at the end of 9 years | $200
Current Book Value | $8500

## Slide 4: Example 3 (cont’d)
Replacement Pump (challenger) | 
Capital investment: | $16,000
Useful life: | 9 years
Depreciation: | MACRS with a 5-year tax life
Annual Expenses | 
Operating and maintenance | $3,000
Taxes and insurance ($16,000 x 2%) | $320
 | $3,320
Present Market Value | $16,000
Estimated Market Value at the end of 9 years | $3,200
Effective income tax rate | 40%
MARR (before taxes) | 10%
MARR (after taxes) | 6%

## Slide 5: Example 3: Before-Tax Analysis
Defender Investment
  Opportunity Cost = Current Market Value = $750
  Salvage Cost = $200
Yearly Total Expenses = $5,340
NAC(9) of Defender=
  $750(A/P,10%,9) - $200(A/F,10%,9) + $5,340
  = $5,455

## Slide 6: Example 3: Before-Tax Analysis (cont’d)
Challenger Investment
  Initial Investment = $16,000
  Salvage Value = $3,200
Yearly Total Expenses = $3,320
NAC(9) of Challenger =
  $16,000 (A/P,10%,9) - $3,200(A/F,10%,9) + $3,320
= $5,862
Therefore, the defender should be kept one more year.

## Slide 7: Example 3: After Tax Analysis
Before-tax analysis is often not valid because of
  the effect of depreciation
  the effect of any significant gain or loss upon disposal
on income taxes.
Therefore, an after-tax analysis should always be done to evaluate the benefit of replacement.

## Slide 8: Example 3: After-Tax Analysis
Defender Investment (at time 0)
  Suppose we sell the defender now.
    Market Value (MV) = $750
    Depreciation per Year = $17,000/9 = $1889
    Current BV = $17000 - (1889/2) - 1889 - … -1889 = $8,500
    Taxable Gain from Salvage = MV - BV = $750 -$8,500 = -$7,750
    Tax on Gain = 0.4 (-$7,750) = -$3,100
  AT Opport. Cost = MV-Tax = $750 -(-$3,100) = $3,850
Therefore, by choosing not to sell the defender, we
incur an after-tax opportunity investment of $3,850

## Slide 9: Note
Note: For some reason, the chapter in your book on Replacement Analysis in the book incorrectly calculates investments in section 9-4 and in all other examples and problems. I have contacted the authors and they are fixing the problems.

## Slide 10: Example 3 (cont’d)
Revenue (in year 1)
  Given
    Before-Tax Revenue = -$5,340
    Depreciation = $1,889 => Book Value = $8,500-$1,889 = $6,611
    Taxable Income = - BT Revenue - Depreciation =
    -$5,340 - $1,889 = -$7,229
    Income Taxes at 40% = (-$7,229)x0.40 = -$2,892
  After-Tax Revenue = BT Revenue - Tax =
  -$5,340 - (-$2,892) = -$2,448

## Slide 11: Example 3 (cont’d)
For year 2, ... ,8, AT Revenue = BT Revenue - Tax
where Tax = Taxable Income x Tax Rate
where Taxable Income = BT Revenue - Depreciation

## Slide 12: Example 3 (cont’d)
Income (in final year 9)
  Given
    Before-Tax Revenue = -$5,340
    Depreciation = $0
    Salvage Value = $200
    Book Value = $0
    Taxable Income = (- BT Revenue - Depreciation)
    + (Salvage Value - Book Value) =
    ( -$5,340 - $0 ) + ($200 - $0) = -$5,140
    Income Taxes at 40% = (-$5,140)x0.40 = -$2,056
  After-Tax Revenue = BT Revenue + Salvage - Tax =
  -$5,140 - (-$2,056) = -$3,084

## Slide 13: ATCF for the Defender
After-Tax NAC using 6% =$3,333

## Slide 14: ATCF for the Challenger
After-Tax NAC using 6% =$3,375

## Slide 15: Lessons from Example 3
Before-Tax and After-Tax Analysis can yield different results. When taxes play a role in cash flows, an after-tax analysis should be performed.
The after-tax NAC of the challenger and the defender are very close ($3,375 vs $3,333). In such cases, other factors (such as the improved reliability of the new pump, productivity loss due to training, etc. ) can be considered

## Slide 16: Example 4: Unknown Useful Lives
New Forklift Truck (challenger)
  Capital investment = $20,000
  For the next five years,
  Estimated MV and Annual Expenses
  Year 1 $15,000 $2,000
  2 $11,250 $3,000
  3 $8,500 $4,620
  4 $6,500 $8,000
  5 $4,750 $12,000
  Effective income tax rate = 40%
  MARR (before taxes) = 10%
  MARR (after taxes) = 6%

## Slide 17: Example 4: Before-Tax Economic Life
The minimum NAC is achieved if we keep the asset three years
Recall that NAC(k) =
(MV(0) + l=1 k A(l )(P/F, i, l ) -MV(k)(P/F,i,k) ) (A/P, i, k )

## Slide 18: Note
It is not uncommon for the before-tax and the after-tax economic lives to be the same
For this reason, many engineers confine their attention to the before-tax economic life only.

## Slide 19: Example 4: Compare against Defender
Current Forklift Truck (defender)
  Capital investment = $13,000, two years ago
  For the next five years,
  Estimated MV and Annual Expenses
  Year 0 $5,000
  1 $4,000 $5,500
  2 $3,000 $6,600
  3 $2,000 $7,800
  4 $1,000 $8,800
  MARR (before taxes) = 10%

## Slide 20: Example 4: BT Econ. Life of Defender
NAC(1) = $5,000 (A/P, 0.1, 1) +$5,500
- $4,000 (A/F, 0.1, 1)
= $5,000 (1.1) + $5,500 - $4,000 = $7,000
NAC(2) = $5,000 (A/P, 0.1, 2) + $5,500 +
$1,100 (A/G, 0.1, 2) - $3,000 (A/F, 0.1, 2)
= $5,000 (0.5762) + $5,500 +
$1,100 (0.4762) - $3,000 (0.4762 ) = $7,476

## Slide 21: Example (cont’d)
The minimum NAC is achieved if we keep the asset one more year.

## Slide 22: Marginal Cost
It is sometimes desirable to keep the asset longer than its economic life.
To determine how long we should keep a defender, we look at the marginal cost
The marginal cost is the cost of keeping the defender an additional year.

## Slide 23: Marginal Cost (cont’d)
It is calculated by finding the increase in NPW of the total cost from the additional year and then converting this to a future worth at the end of year k.
The Marginal Cost in year k =
[NPC(k)-NPC(k-1)](F/P, i, k)
An alternative(easier) way to calculate the marginal cost is
MV(k-1) (F/P, i, 1 ) - MV(k) + A(k)

## Slide 24: Example 4 (cont’d)
MC(1) = $5,000 (F/P, 0.1, 1) - $4,000 + $5,500 = $7,000
MC(2) = $4,000 (F/P, 0.1, 1) - $3,000 + $6,600 = $8,000

## Slide 25: Example 4 (cont’d)

## Slide 26: Lessons from Example 4
Keep the old truck at least one more year.
Also note that the marginal cost for keeping the truck a second year is $8,000, which is still less than the minimum NAC for the challenger (i.e., $8,598)
And, the marginal cost for keeping the defender a third year and beyond is greater than $8,598, minimum NAC for the challenger.
Therefore, based on current data, it would be most economical to keep the defender for two more years and then replace it with the challenger.

## Slide 27: Summary
The MV of the defender must not be deducted from the purchase price of the challenger when using the outsider viewpoint
Sunk costs must not be considered in the analysis
Economic life of the defender is often one year. The marginal cost of the defender should be compared with the minimum NAC of the challenger to answer “when to dispose” questions.
Technological changes will often bring new challengers. Analysis must then be repeated.