## Slide 1: Cut the Lot Size
What can we do if the bottleneck has moved outside the plant?

## Slide 2: Jonah: Cut the lot size
The lot size is the amount produced for each machine setup
What encourages us to use large lot sizes?
What encourages us to use small lot sizes?
Under what circumstances can we cut the lot size without reducing throughput?

## Slide 3: What encourages us to use large lot sizes?
The lot size is the amount produced for each machine setup
A setup uses time on the constraint
Larger lots cause fewer setups
To maximize throughput select the lot size as large as possible
One Remedy: Reduce the setup time

## Slide 4: What encourages us to use small lot sizes?
Small lots reduce cycle time
WIP is proportional to cycle time
Reducing cycle time reduces inventory

## Slide 5: When can we reduce lot size without reducing throughput?
When the setup time is small
When the constraint is outside the manufacturing process
  (when there are no internal constraints)
Set the lot size as small as possible while not allowing a non-bottleneck to become a bottleneck

## Slide 6: Large Lot, High Inventory Manufacture

## Slide 7: Consequences
Lot size=1000
Cycle Time=3.4 mo. Time to complete =3.4 mo. @720 hrs/mo.
WIP=1000 units

## Slide 8: Small Lot, Low Inventory Manufacture

## Slide 9: Consequences
Lot size=200
Cycle Time=0.7 mo.
Time to complete =1.8 mo. @720 hrs/mo.
WIP=400 units

## Slide 10: Benefits of small lot, low inventory manufacture

## Slide 11: Summary of The Goal
What is the Goal?
What do you think should be
the goal?
Describe the Goal
What Financial
Measures
of Making Money?
Measures Describe the
How do these measures
What Operational
Goal?
relate to the goal?
How do the
measures
relate to
decisions
made in the
plant?
What is the combined
effect of dependent
events and statistical
fluctuations?
What is a bottleneck, and
how do you find it?
How can you increase the
capacity of a bottleneck?
What does it cost to
have a bottleneck idle?
How can we keep
from having the
bottleneck idle?
What do we do
when bottleneck
has moved out of
the plant?
What are the advantages
of smaller lot sizes?
What do we
do when
management
measures tell the
wrong story?