## Slide 1: Lecture 14 – Queuing Systems
Topics
Basic structure and components
Performance measures
Steady-state analysis and Little’s law
Birth-death processes
Single-server and multi-server examples
Flow balance equations
Notes: <number>

## Slide 2: Structure of Single Queuing Systems
Input
source
Queue
Service
mechanism
Arriving
customers
Exiting
customers
Note
Customers need not be people; other possibilities include parts, vehicles, machines, jobs.
Queue might not be a physical line; other possibilities include customers on hold, jobs waiting to be printed, planes circling airport.
Notes: <number>

## Slide 3: Components of Model
Input Source The size of the “calling population”
may be modeled as infinite or finite.
Calculations are easier in the infinite case and
in many cases this is a reasonable approximation
(bank, pizza parlor, blood bank).
Queuing Discipline First-come first-served (FCFC or FIFO) is the most frequent assumption, but priority ordering is important in some settings.
Service Mechanism One or more servers may be placed in parallel.
Notes: <number>

## Slide 4: Queuing Applications
System Arrival Process Service Process
Bank Customers Arrive Tellers serve customers
Pizza Orders are phoned Orders are driven to
parlor in customers
Blood Pints of blood arrive Patients use up
bank via donation pints of blood
Shipyard Damaged ships sent Ships are repaired
to shipyard for repair & return to sea
Printers Jobs arrive from Documents are
computers printed
Notes: <number>

## Slide 5: Typical Performance Questions
What is the ...
1. average number of customers in the system?
2. average time a customer spends in the system?
3. probability a customer is rejected?
4. fraction of time a server is idle?
These questions are aimed at
characterizing complex systems.
Analyses used to support decision-making.
In queuing (and most analyses of complex stochastic
systems), design takes the form of asking “what if ”
questions rather than trying to optimize the design.
Notes: <number>

## Slide 6: Multiple Servers, Single Queue
What is average wait in the queue?
What is average time in the system?
Notes: <number>

## Slide 7: Multiple Servers, Multiple Queues
What is average wait in the queue?
What is average time in the system?
Notes: <number>

## Slide 8: Notation and Terminology
N(t ) = # of customers in the system at time t  0
Pk(t ) = probability exactly k customers in system
at time t, given # in system at time 0
s = # of parallel servers
k = mean arrival rate
(expected # of arrivals per unit time)
k = mean service rate
(expected # of departures per unit time)
(Both k and k assume k customers are in system)
Notes: <number>

## Slide 9
If there are s servers, each with the same service rate, then
k = s for k  s and k = k for 0  k < s.
s = customer service capacity per unit time
= /s = utilization factor (traffic intensity)
The systems we study will have  < 1 because otherwise
the # of customers in the system will grow without bound.
We will be interested in the steady-state behavior
of queuing systems (the behavior for t large).
Obtaining analytical results for N(t ), Pk(t ), . . .
for arbitrary values of t (the transient behavior)
is much more difficult.
If k does not depend on # of customers in system, k = .
Notes: <number>

## Slide 10: Notation for Steady-State Analysis
k = probability of having exactly k customers in the system
L = expected number of customers in the system
Lq = expected queue length
(doesn’t include those being served)
W = expected time in system, including service time
Wq = expected waiting time in the queue
(doesn’t include service)
Notes: <number>

## Slide 11: Little’s Law
For any queuing system that has a steady state
and has an average arrival rate of ,
L = W
For example, if the average waiting time is 2 hours
and customers arrive at a rate of 3 per hour then,
on average, there are 6 customers in the system.
Similarly, Lq = Wq
If k =  for all k  1 then W = Wq + 1/
(1/ is the mean
service time here)
Notes: <number>

## Slide 12: Benefit of Little’s Law
These three relationships allow us to calculate all four quantities L, Lq, W and Wq
(once one of them is known).
L = W requires no assumptions about arrival or service time distributions, the size of the calling population, or limits on the queue.
Notes: <number>

## Slide 13: Birth and Death Processes
Applications in a variety of areas, but in queuing “birth” refers to the arrival of a customer while “death” refers to the departure of a customer.
Recall, N(t ) = # of customers in the system at time t.
Assumptions
Given that N(t ) = k, the pdf governing the remaining time until the next birth (arrival) is
exp(k) k = 0, 1, 2, . . .
Given that N(t ) = k, the pdf governing the remaining time until the next death
(service completion) is exp(k) k = 1, 2, . . .
All random variables are assumed to be independent.
Notes: <number>

## Slide 14: Transition Rate Diagram
We will investigate steady-state (not transient) results
for birth-death processes based on the
Expected rate in = Expected rate out principle
1
3
2
3
0
1
2
2
1
0
Let k = steady-state probability of being in state k.
Notes: <number>

## Slide 15: Balance Equations – Section 15.5
Flow into 0  11 = 00  flow out of 0
Flow into 1  00 + 22 = (1 + 1)1  flow out of 1
Flow into 2  11 + 33 = (2 + 2)2  flow out of 2
•
•
•
Flow into k
k-1k-1 + k+1k+1 = (k + k)k  flow out of k
Notes: <number>

## Slide 16
=

0

1

=

1

2

+
1

2
 – 
=

1

2

=

1

0

2

1

. . .
,
Thus k = Ck0 , k = 1, 2, . . . and kk = 1
so (C0 + C1 + C2 + • • • )0 = 1 or 0 = 1 / (1 + k Ck)
= 0
Notes: <number>

## Slide 17: Some Steady-State Results
Once we have calculated the k’s we can find:
L =  kk = expected # of customers in the system
Lq =  (k–s)k = expected # of customers in queue
Ls = L – Lq = expected # of customers in service
 =  kk = average (effective) arrival rate
E = Ls / s = efficiency of system (utilization)

k=1

k=s+1

k=0
Notes: <number>

## Slide 18: Queuing Example with 3 Servers
Assume
Average arrival rate:  = 5/hr
Average service rate:  = 2/hr
Arriving customer balks when 6 are in system.
4. Steady-state probabilities:
State | 0 | 1 | 2 | 3 | 4 | 5 | 6
Component | 0 | 1 | 2 | 3 | 4 | 5 | 6
Probability | 0.068 | 0.170 | 0.212 | 0.177 | 0.147 | 0.123 | 0.102
Notes: <number>

## Slide 19: Determining System Characteristics
What is the probability that all servers are idle?
Pr{all servers idle} = 0 = 0.068
What is the probability that a customer will not have to wait?
Pr{no wait} = 0 + 1 + 2 = 0.45
What is the probability that a customer will have to wait?
Pr{wait} = 1 – Pr{no wait} = 0.55
What is the probability that a customer balks?
Pr{customer balks} = 6 = 0.102
Notes: <number>

## Slide 20: Steady-State Measures for Example
Expected number in queue:
Lq = 14 + 25 + 36 = 0.700
Expected number in service:
Ls = 1 + 22 + 3(1 – 0 – 1 – 2) = 2.244
Expected number in the system:
L = Lq + Ls = 2.944
Efficiency of the servers:
E = Ls /s = 2.244/3 = 0.748 or 74.8%
Notes: <number>

## Slide 21: Little’s Law with Average Arrival Rate
Applying Little’s Law with , we can calculate
W = L /  & Wq = Lq / 
Expected waiting time in the system
Expected waiting time in the queue
Results assume that steady state will be reached.
Notes: <number>

## Slide 22: Example with 3 Servers (cont.)
To compute average waiting times we must first find the average arrival rate:
 =  kk where k =  = 5 (k = 0,1,…,5) and
k = 0 (k > 5), simplifies to
= (0 + 1 + 2 + 3 + 4 + 5)
= (1 – 6) = 5(1 – 0.102) = 4.488 / hour

k=0
Consequently,
Ws = Ls /  = 0.5 hours
Wq = Lq /  = 0.156 hours
W = L /  = 0.656 hours
Notes: <number>

## Slide 23: M/M/1 Queue
“M ” stands for Markovian, meaning
exponential inter-arrival & exponential service times.
M / M / 1
arrival service # of
process process servers
2
1
0

3






. . .

so, k = , k = 0,1,…
k = , k = 1,2,…
where  = 
Utilization factor or
traffic intensity
Notes: <number>

## Slide 24: Derivation of Steady-State Probabilities
Thus, 0 = 1 –  and k = k(1 – ).
provided1, i.e., 
Notes: <number>

## Slide 25: Performance Measures for M/M/1 Queue
L = provided   


Lq = L  (1  0) =






=
From Little’s law, we know
W =
1

L and
Wq
=
1

Lq or
W =
1


and Wq =


Notes: <number>

## Slide 26
The important thing is not the specific M/M/1 formulas, but the methodology used to find the results.
Model the system as a birth-and-death process and construct the rate diagram.
Depending on the system, defining the states may be the first challenge.
Develop the balance equations.
Solve the balance equations for k, k = 0, 1, 2, . . .
Use the steady-state distribution to derive L and Lq and, use Little’s law to get W and Wq .
Methodology vs. Formulas
Notes: <number>

## Slide 27: Example of M/M/1/2/2 Queue
A maintenance worker must keep 2 machines in working order. The 2 machines operate simultaneously when both are up.
The time until a machine breaks has an exponential distribution with a mean of 10 hours.
The repair time for the broken machine has an exponential distribution with a mean of 8 hours.
The worker can only repair one machine at a time.
Notes: <number>

## Slide 28: Evaluating Performance
Model the system as a birth-and-death process.
Develop the balance equations.
Calculate the steady-state distribution k .
Calculate and interpret L, Lq, W, Wq .
What is the proportion of time the repairman is busy ?
What is the proportion of time that a given machine, e.g., machine #1, is working ?
Notes: <number>

## Slide 29: State-Transition Diagram
 = rate at which a single machine breaks down
= 1/10 hr
 = rate at which machines are repaired
= 1/8 hr
State of the system = # of broken machines.
2
1


2

0
2
Rate network:
Notes: <number>

## Slide 30: Balance Equations for Repair Example
1 = 20
20 + 2 = ( +  )1
1 = 2
0+ 1+ 2
Ck =
k-1… 0
k … 1
k = Ck0 and 0 = 1 /  Ck
We can solve these balance equations for 0, 1 and 2,
but in this case, we can simply use the formulas
for general birth-and-death processes:
2
k=0
state 0
state 1
state 2
normalize
Notes: <number>

## Slide 31
Here, 0 = 2 1 = 
1 =  2 = 
    2 = 0
L = 00 + 11 + 22 = 1.072 (avg # machines in system)
Lq = 01 + 12 = 0.33 (avg # waiting for repair)
Notes: <number>

## Slide 32
Proportion of time that machine #1 is working
= 0 +
1
2
1 = 0.258 +
1
2
(0.412) = 0.464
Proportion of time repairman is busy = 1 + 2 = 0.742
average arrival rate  =
    kk = 00 + 11 + 22
= (2)0 + 1 = 0.0928


k = 0
= 11.55 hours
Average amount of time
that a machine has to wait
to be repaired, including
the time until the repairman
initiates the work.
= 3.56
hours
Average amount of time that a
machine has to wait until the
repairman initiates the work.
Notes: <number>

## Slide 33: Excel Add-in for M/M/1/2/2 Queue
Notes: <number>

## Slide 34: Multi-Channel Queues – M/M/s
Additional measures of performance
Efficiency: E = 
Pr{ Tq = 0 } = k=0,s-1 k
Pr{ Tq > t } = (1 – Pr{ Tq = 0 })e-s(1-)t for t > 0
Notes: <number>

## Slide 35: M/M/s Queue
Notes: <number>

## Slide 36: Telephone Answering System Example
Situation:
A utility company wants to determine a staffing plan for its customer representatives.
Calls arrive at an average rate of 10 per minute, and it takes an average of 1 minute to respond to each inquiry.
Both arrival and service processes are Poisson.
Problem: Determine the number of operators that would provide a “satisfactory” level of service to the calling population.
Analysis:  = 10, 1/ = 1;  = /s < 1 or s > / = 10
Notes: <number>

## Slide 37: Comparison of Multi-Server Systems
Measure | M/M/11 | M/M/12 | M/M/13
Lq | 6.821 | 2.247 | 0.951
Wq | 0.682 | 0.225 | 0.0.95
E | 0.909 | 0.833 | 0.767
Pr{ Tq = 0 } | 0.318 | 0.551 | 0.715
Pr{ Tq > 1 } | 0.251 | 0.061 | 0.014
Notes: <number>

## Slide 38: Machine Processing with Limited Space for Work in Process
Parts arrive at a machine station at the rate of 1.5/min on average.
The mean time for service is 30 seconds.
Both processes are assumed to be Poisson.
When the machine is busy, parts queue up until there are 3 waiting. At that point arrivals sent for alternative processing.
Goal: Analyze the situation under the criteria that no more than 5% of arriving parts receive alternative processing and that no more than 10% of the parts that are serviced directly spend more than 1 minute in the queue.
Notes: <number>

## Slide 39: Parameters for Machine Processing Queuing System
Number of servers: s = 1
Maximum number in system: K = 4
Size of calling population: N = 
Arrival rate:  = 1.5/min
Service rate:  = 2/min
Utilization:  = /= 0.75
Model: M/M/1/4
Notes: <number>

## Slide 40: M/M/1/K Queue, 
Measure

M
/
M
/1/
K

M
/
M
/1





0
1


1


K

1
1
–


n
, 1

n

K

0

n

0

n

K

0

K
0
P
B

(
1


K
)
1


K

1

L
q

2
[(
K

1
)

K

K

K

1

1
]
(
1


)(
1


K

1
)

2
1


L
s

(1
–

K
)

L

1
–

–
(
K

1
)

K

1
1


K

1

1





(1
–

K
)


E

(1
–

K
)

Notes: <number>

## Slide 41: Excel Add-in for M/M/1/4 Queue
Notes: <number>

## Slide 42: Solution for M/M/1/4 Model
Parameters
 = 1.5/min,  = 2/min
 = /= 0.75
K = 4
Steady state probabilities (see page 566 in text)
0 = (K) = (1 – 0.75) / (1 – 0.755) = 0.25 / 0.7627
= 0.328
k = 0 k = (0.328) (0.75k); k = 1,…,K
1 = 0.246, 2 = 0.184, 3 = 0.138, 4 = 0.104
Notes: <number>

## Slide 43: Solution for M/M/1/4 Model (cont’d)
Balking probability: PF = 4 = 0.104 or 10.4%
(does not meet 5% goal)
Average arrival rate:  = (1 – PF) = 1.344/min
L = 1.444
W = 1.074 min
E = (1 – PF) = 0.75(1 – 0.104) = 0.672 or 67.2%
Pr{Tq > 1} = 0.225 (see text for computations; does not meet 10% goal)
Notes: <number>

## Slide 44: Add Second Machine – M/M/2/5 Model
New results
PF = 0.0068,  = (1 – 5) = 1.49
L = 0.85, W = 0.57 min
E = 37.2%
Pr{Tq > 1} = 0.049 or 4.9%
This solution meets our original goals with the percentage of balking parts now less than 1% and the probability of a wait time greater than 1 minute less than 5%
Notes: <number>

## Slide 45: What You Should Know About Queuing Systems
The major components
The 5-field notation
How to use Little’s law
Components of a Markov queuing system
The important performance measures
How to compute performance measures
Notes: <number>