## Slide 1: Lecture 14 – Queuing Networks
Topics
Description of Jackson networks
Equations for computing internal arrival rates
Examples: computation center, job shop
Non-Markovian networks
Notes: <number>

## Slide 2: Structure of Single Queuing Systems
Input
source
Queue
Service
mechanism
Arriving
customers
Exiting
customers
Note
Customers need not be people  parts, vehicles, machines, jobs.
Queue might not be a physical line  customers on hold, jobs waiting to be printed, planes circling airport.
Notes: <number>

## Slide 3: Queuing Networks
In many applications, an arrival has to pass through a series of queues arranged in a network structure.
Notes: <number>

## Slide 4: Jackson Network Definition
1. All outside arrivals to each queuing station in the network must follow a Poisson process.
2. All service times must be exponentially distributed.
3. All queues must have unlimited capacity.
4. When a job leaves one station, the probability that it will go to another station is independent of its past history and is independent of the location of any other job.
In essence, a Jackson network is a collection of connected M/M/s queues with known parameters.
Notes: <number>

## Slide 5: Jackson’s Theorem
Each node is an independent queuing system with Poisson input determined by partitioning, merging and tandem queuing example.
Each node can be analyzed separately using M/M/1 or M/M/s model.
Mean delays at each node can be added to determine mean system (network) delays.
Notes: <number>

## Slide 6: Computation of Input Rate
Let i = external arrival rate to station i = 1, . . . , m
ki = probability of going from station k to i in network
i = total input to station i
In steady state there must be flow balance at each station.
Notes: <number>

## Slide 7: Element of a Queuing Network
Notes: <number>

## Slide 8: Jackson Networks
Two-stage example.
Each station is M /M /s queue.
Notes: <number>

## Slide 9: Matrix Form of Computations
Property 1: Let  be the m  m probability matrix that describes the routing of units within a Jackson network, and let i denote the mean arrival rate of units going directly to station i from outside the system. Then
 = (I – )–1
where  = (1,…,m) and the components of the vector l give the arrival rates into the various station; that is, i is the net rate into station i.
Note: Unlike the state-transition matrix used for Markov chains, the rows of the  matrix here need not sum to one; that is j ij ≤ 1
Notes: <number>

## Slide 10: Simplification of Network
After the net rate into each node is known, the network can be decomposed and each node treated as if it were an independent queuing system with Poisson input.
Property 2: Consider a Jackson network comprising m nodes. Let Ni denote a random variable indicating the number of jobs at node i (the number in the queue plus the number in service). Then,
Pr{ N1 = n1, …, Nm = nm } = Pr{ N1 = n1}  …  Pr{ Nm = nm }
and
Pr{ Ni = ni} for all ni = 0, 1, … can be calculated using the equations for independent M/M/s seen previously.
Notes: <number>

## Slide 11: Computation Center Example
A high performance computation center is composed of 3 work stations comprising: (1) input processors, (2) central computers, and (3) a print center.
All jobs submitted must first pass through an input processor for error checking before moving on to a central processor  80% go through and 20% are rejected.
Of the jobs that pass through the central processor, 40% are routed to a printer.
Jobs arrive randomly at the computation center at an average rate of 10/min. To handle the load, each station may have several parallel processors.
Notes: <number>

## Slide 12: Data for the Computation Center
We know from previous statistics that the time for the three steps have exponential distributions with means as follows:
10 seconds for an input processor
5 seconds for a central processor
70 seconds for a graphic processor
All queues are assumed to have unlimited capacity.
Goal
Model system as a Jackson network. Find the minimum number of processors of each type and compute the average time require for a job to pass through the system.
Notes: <number>

## Slide 13: Arrival Rate Computations
Using general equation:
With m = 3, 1 = 10, 12 = 0.8, 23 = 0.4
we get:
1 = 
2 = 1 = 
3 = 0.42 = 
Notes: <number>

## Slide 14: I/O Data for the Computation Center
Input
Central
System measure
processor
processor
Printer
External arrival rate, i
10/min
0
0
Total arrival rate, i
10/min
8/min
3.2/min
Service rate, i
6/min
20/min
0.857/min
Minimum channels, si
2
1
4
Traffic intensity, i
0.833
0.400
0.933
Notes: <number>

## Slide 15: Results for Computation Center
Input
Central
Printer
Measure
processor
processor
station
Total
Model
M/M/2
Lq
3.788
0.267
12.023
16.077
Wq
0.379
0.033
3.757
4.169
L
1.667
0.400
3.734
5.801
Ws
0.167
0.050
1.167
1.384
M/M/1
M/M/4
Notes: <number>

## Slide 16: Job Shop Example
Scenario
Three products
Four machines: A, B, C, D
Each class takes different route
Data
Product | Order rate | Route
1 | 30/mo | A-B-D-F
2 | 10/mo | A-B-E-F
3 | 20/mo | A-C-E-F
Notes: <number>

## Slide 17: Network for Shop Shop
Notes: <number>

## Slide 18: Results for Job Shop Example
Measure | A | B | C | D | E | F
 | 60 | 0 | 0 | 0 | 0 | 0
 | 25 | 22 | 29 | 11 | 23 | 20
s | 3 | 2 | 1 | 3 | 2 | 4
Model | M/M/3 | M/M/2 | M/M/1 | M/M/3 | M/M/2 | M/M/4
 | 60 | 40 | 20 | 30 | 30 | 60
 | 0.800 | 0.909 | 0.690 | 0.909 | 0.652 | 0.750
L | 4.989 | 10.476 | 2.222 | 11.059 | 2.270 | 4.528
W | 0.083 | 0.262 | 0.111 | 0.369 | 0.076 | 0.075
Lq | 2.589 | 8.658 | 1.533 | 8.332 | 0.965 | 1.528
Wq | 0.043 | 0.216 | 0.077 | 0.278 | 0.032 | 0.025
Notes: <number>

## Slide 19: System Performance Measures
Manufacturing lead time
  – Average time a product spends in the system
  – Summation of time spent in each M/M/s system
Work-in-process (WIP) inventory
  – Computed from Little’s law
  – WIP = (lead time)  (order rate)
Questions: Can we sum L in each M/M/s queue to get WIP ?
Notes: <number>

## Slide 20: System Performance for Job Shop
 | Order rate |  | Lead time | Queue time | WIP
Product | (per mo.) | Route | (mo.) | (mo.) | (units)
1 | 30 | A-B-D-F | 0.789 | 0.563 | 23.67
2 | 10 | A-B-E-F | 0.496 | 0.317 | 4.96
3 | 20 | A-C-E-F | 0.345 | 0.177 | 6.91
WIP determined with Little’s law = (lead time)  (order rate).
Results show a marked difference between the products in terms of lead time and WIP since product 1 passes through both stations B and D.
Notes: <number>

## Slide 21: Non-Markov Networks
View each station as an GI/G/1 queue.
 A Jackson network can be used to approximate this network.
Assume we have a network with K classes of customers.
Each class k K has a fixed routing through the network.
Unlimited capacity at each node.
Arrival and service processes not known, but means and standard deviations of interarrival times and service times are known.
Notes: <number>

## Slide 22: Non-Markov Network Example
Let msi = mean processing time at station i for i = 1, 2, 3
si = standard deviation of processing time at station i
Data:
Notes: <number>

## Slide 23: Example (continued)
Mean time between arrivals is ma = 5 minutes so  = 0.2/min.
Mean time between departures at station 1, and equivalently the mean time between arrivals at stations 2, is the same  ma.
Similarly, the departures from stations 2 and 3 all have the same mean, ma.
Standard deviation of the time between departures d1, d2 and d3, will differ, however, because of the joint effects of arrival and service variability on departure variability.
The approximate relation is
cd2 = 2cs2 + (1 – 2)ca2 and d = cd ma
The departure coefficient of variation is the same as the arrival coefficient of variation of the next stage.
Notes: <number>

## Slide 24: Results for Non-Markov Network Example
Queues can be analyzed sequentially starting with station 1 using the formula
W
q
(
GI
/
G
/
1
)

c
a
2
+
c
s
2
2






W
q
(
M
/
M
/
1
)
At each station: W = Wq + 1/
Use Little’s law to find L and Lq with  = 0.2/min for each station.
Notes: <number>

## Slide 25: What You Should Know About Queuing Networks
The assumptions underlying a Jackson network.
How to compute the internal arrival rates.
How to evaluate performance of a Jackson network.
The extent to which non-Poisson networks can be analyzed.
Notes: <number>