## Slide 1: Unit Flow
In the long run, the product flow through each operation must be proportional to the output flow of the process

## Slide 2: Operation Flow Depends on the Flow of Finished Goods
Finished Good: A completed product leaving the process
The total flow of product through an operation is proportional to the flow of finished goods
Unit Flow: The number of units entering an operation per unit of finished good

## Slide 3: Find the flow in each operation
Consider a process with And nodes
Unit flow is proportional to the flow leaving the final operation
Unit flow depends on the operations that follow in the process
Flow through
operations
Flow of finished goods

## Slide 4: Factors that change flow at an operation
Grouping factor: the number of items that are grouped for subsequent processing
Scrap rate: the proportion of input items discarded
Flow ratio: flow leaving divided by flow entering

## Slide 5: We want to compute the unit flow for each operation
u
i
(unit flow) The number of items passing
into
op
eration
i
for each unit of
finished
product.

## Slide 6: The Unit Flow depends on the next operation

## Slide 7: Process for finding unit flows
Assign the unit flow 1 to the output of the process
Work backwards to find all other unit flows

## Slide 8: What if all grouping factors are 1 and scrap rates are 0?
All unit flows are 1

## Slide 9: Compute unit flows
3
2
1
5
6
7
8
R2
R3
A
A
4
R1
u’8 =1
u8=1/(1 - 0.1)
=1.111
u7=1.1
1*3/(1 - .3)
=4.742
Unit Flow
1.929
1.736
3.086
1.389
5.879
5.291
4.762
1.111

## Slide 10: Example: Line with defects and inspection

## Slide 11: First compute scrap at each operation
Scrap rate
= 1-(1-.1)6
= 1-(.9)6
= .469
Scrap rate = 0

## Slide 12: Compute unit flows
u7 = 1/(1-.469)
= 1.88
ui = 1.88 for i = 1 … 6